## Slide 1: Android App Controlled RC Car
Eric Junkins
Joe Wroe
Jean-Christophe Owens
Vilok Krishnan

## Slide 2
Development Tools Used
Trello
  Project Tracking
Github
  Version Control
Android Studio
  Android IDE
Raspberry Pi 3
  Hardware communcation

## Slide 3: Overview
Battery pack
Steering Servo
Speed Controller
Receiver
Steering Axel
Drive Shaft
Controller

## Slide 4: Overview
Battery pack
Steering Servo
Speed Controller
Steering Axel
Drive Shaft
Controller

## Slide 5: Design Aspects
Reverse Engineer receiver signals (no documentation )
Replace receiver with Raspberry Pi to mimic signals
Write Android App to control Raspberry Pi over remote signal

## Slide 6: Reverse Engineer Signals

## Slide 7: Signals
1.5ms
10ms
1.0ms
2.0ms
Periodic at 10ms
3.3V Digital
Base signal at 1.5ms (do nothing)
Identical signals to both systems
Turn left or throttle backward (max)
Turn right or throttle forward (max)
3.3V

## Slide 8: Physical System
Battery pack
Steering Servo
Speed Controller
Steering Axel
Drive Shaft
Android App
PiCam
Rtsp web address

## Slide 9: Raspberry Pi Signals
Use the GPIO pins to output square pulse based on input from App
2 Separate Pis, one for each mechanical system on car
Master Pi – communicate to/from App
  Slave Pi – takes commands from Master Pi
Master Pai Mei
-Kill Bill (2003)

## Slide 10: Networking Signals
Use WIFI sockets to communicate
  ~72MBPS (necessary for video)
Mastery Pi config change to broadcast WIFI
  App/Slave Pi will connect to network
Send PiCam stream to rtsp web address:
  rtsp://192.168.1.80:8554/myPicam/Stream.mp4

## Slide 11: A Few Other Things To Do
Init Scripts on Main Pi:
  Start pigpiod daemon
  Start python script listening for socket connection to Slave Pi and App
Init Script on Slave Pi:
  Start pigpiod daemon
  Initialize python script with wifi socket to Master Pi
Haptic Feedback on App
Joysticks
Video player
Speedometer on App

## Slide 12: Android App
Connects to Wifi Socket on RPi
Status of Wifi Socket
Steering Joystick
Throttle Joystick
Throttle Speedometer
Steering Speedometer
Video Player

## Slide 13: Other Features/Future Implementations
Get PiCam Stream to work
Joystick override with accelerometers in phone mode
Simple voice command (Snowboy Hotword Detection)
  Locally run, no internet server
  Trainable

## Slide 14: Demo